## Slide 1: MBSD Lecture 0
Overview

## Slide 2: Course Goals
Present and emphasize MBSD approach
  Simple models
  Complex system
  Basic control
  Iterative refinement
Utilize simulation tools
  Matlab
  Simulink
  Stateflow
Notes: Needs update

## Slide 3: Course Outline
Simple Series Electric Vehicle
  Model hierarchy
  Ideal Component Models
  Controls
Improved Component Models
  Inefficiencies
  Experimental Data
Improved Controls
Notes: Needs update

## Slide 4: Model Overview - System
CAN Bus
Driver
Plant
Controller
Notes: Needs update

## Slide 5: Model Overview - Plant
MGA
MGB
Engine
Data Logging
Vehicle Solver
Battery
System Components
Notes: Needs update

## Slide 6: Model Overview - Plant
Mechanical shaft
Mechanical shaft
Notes: Needs update

## Slide 7: Model Overview - Plant
Electrical Connections
Notes: Needs update

## Slide 8: Model Overview - Plant
Network Connections - CAN
Notes: Needs update

## Slide 9: Model Overview - Vehicle
Linear Momentum
Angular Momentum
Notes: Needs update

## Slide 10: Model Overview - MG
Torque Data
Conversion Efficiency Data
Notes: Needs update

## Slide 11: Model Overview – Battery
OCV Data
State of Charge
Conversion Efficiency Data
Notes: Needs update

## Slide 12: Model Overview - Engine
Torque Data
Fuel Consumption Data
Notes: Needs update

## Slide 13: Model Overview - Logging
Plotted Data
Logged Data
Notes: Needs update

## Slide 14: Model Overview - Driver
Speed Trace
Notes: Needs update

## Slide 15: Model Overview - Controller
Powertrain Torque Request
Engine Speed control
Battery Charge Logic
Notes: Needs update

## Slide 16: Model Overview - GentSet
Notes: Needs update

## Slide 17: Results
Vehicle Speed
Battery SOC
Currents
Engine Speed
Notes: Needs update

## Slide 18: MBSD Lecture 1
Getting Started with the High Level System

## Slide 19: Lecture Goals
Getting Started with Simulink
Developing model hierarchy (subsystems)
Establishing CAN bus
Notes: Needs update

## Slide 20: Getting Started
Start Matlab
Make sure you are in the correct directory
Type simulink in the command window
Notes: Needs update

## Slide 21: Getting Started
Make sure all files and folders exist in your directory
This button allows you to choose the directory
Instead of typing Simulink in the command directly you can select this button
Notes: Needs update

## Slide 22: Getting Started
Select Blank model
Notes: Needs update

## Slide 23: Getting Started
Simulink is a graphical programming environment which enables you to link function blocks to create simulations
In the Simulink model window, select library browser
Library Browser
Notes: Needs update

## Slide 24: Getting Started
Get yourself familiar with the libraries and blocks in the library browser
Library
Block
Notes: Needs update

## Slide 25: Getting Started
We will primarily use the following libraries
  Simulink \ Commonly Used Blocks
  Simulink \ Signal Routing
  Simulink \ Lookup Tables
  Simulink \ Sinks
  Simulink \ Sources
  Simscape \ Driveline
  Stateflow
Notes: Needs update

## Slide 26: Getting Started
Save the Simulink model as :
  Series_Hybrid_le1_a
Do not use spaces or variable names in file names
Notes: Needs update

## Slide 27: High Level Model
We will first create the high level plant and controller model
From
  Simulink \ Commonly Used Blocks
Drag three Subsystem blocks into the model
  Driver block
  Controller block
  Vehicle block
Notes: Needs update

## Slide 28: High Level Model
Notes: Needs update

## Slide 29: High Level Model
Rename the upper subsystem
  Driver
The middle subsystem
  Plant
The lower subsystem
  Controller
Notes: Needs update

## Slide 30: High Level Model
You can change the font size by right clicking on each subsystem/Format/Font Style…
Notes: Needs update

## Slide 31: High Level Model
At this high level, signals will be sent out by the Driver, Plant, and Controller
  Driver Torque Request
  Battery State of Charge
  Engine Throttle Request
These signals will be put onto a common bus so that all three subsystems can receive all signals
  Only desired signals will be selected
Notes: Needs update

## Slide 32: High Level Model
Open Model Browser by selecting the arrow
  Shows an outline form of the model
Notes: Needs update

## Slide 33: Driver Subsystem
The Driver receives information
  Speedometer
  Tachometer
  Idiot lights (engine hot, …..)
The Driver sends information
  Torque request (gas/brake pedal position)
  Gear selection
Notes: Needs update

## Slide 34: Driver Subsystem
Open the Driver subsystem by:
  clicking on Driver in Model Browser or
  double click on the Driver block
Delete the wire that connects the In1 block to out1 block
Rename
  In1 to System Signals
  Out1 to Driver Diagnostics
Notes: Needs update

## Slide 35: Driver Subsystem
It is okay to have spaces and returns in labels
The asterisk indicates that the file has not been saved – save file before running the simulation
Notes: Needs update

## Slide 36: Driver Subsystem - CAN
From
  Simulink \ Commonly Used Blocks
Drag in a Bus Selector and a Bus Creator
  The Bus Creator puts signals on the bus
  The Bus Selector extracts them from the bus
Connect the System Signals input to the Bus Selector
Connect the Driver Signals input to the Bus Creator
Notes: Needs update

## Slide 37: Driver Subsystem - CAN
Bus Selector
Bus Creator
Notes: Needs update

## Slide 38: Driver Subsystem - CAN
For now, the Driver is not going to do anything
From
  Simulink \ Commonly Used Blocks
Drag in two Terminators and two Grounds
Connect the two outputs of the Bus Selector to the Terminators
Connect the two inputs of the Bus Selector to the Grounds
Notes: Needs update

## Slide 39: Driver Subsystem - CAN
Name of the signal from the bus selector – currently no signal is attributed to each port. We will later assign a signal to one
Notes: Needs update

## Slide 40: Driver Subsystem - CAN
The symbols for the ground and terminator are pretty obvious – there is no need for them to be labeled
On one of the Terminators
  Right Click
  Select Format
  Deselect Show Block Name
We will do this for many of the blocks
Hide the name of all terminator and ground blocks
Notes: Needs update

## Slide 41: Driver Subsystem - CAN
Notes: Needs update

## Slide 42: Driver Subsystem - CAN
While no signals are being sent by the Driver, the Driver Diagnostics signal should be identified on the bus
On the wire connecting the Bus Creator to the Driver Diagnostics output
  Right Click
  Select Properties
  For the Signal name enter Driver_Diagnostics
  Click OK
Notes: Needs update

## Slide 43: Driver Subsystem - CAN
Notes: Needs update

## Slide 44: Driver Subsystem - CAN
Move the blocks around, enlarge if necessary, and make things look nice
Notes: Needs update

## Slide 45: Controller Subsystem
For now, the controller is not going to do anything
Repeat everything done to the Driver subsystem for the Controller subsystem
  Rename the Out1 to Controller Signals
  Rename the CAN signal to Controller_Signals
Notes: Needs update

## Slide 46: Controller Subsystem
Notes: Needs update

## Slide 47: Plant Subsystem
For now, the Plant is not going to do anything
Repeat everything done to the Controller subsystem for the Plant subsystem
  Rename the Out1 to Plant Diagnostics
  Rename the CAN signal to Plant_Diagnostics
Notes: Needs update

## Slide 48: Plant Subsystem
Notes: Needs update

## Slide 49: High Level
Return to the top level of the model
Increase the size of the subsystems to make them legible
Drag in a Bus Creator
  Double click of the Bus Creator
  Change the number of inputs to 3
  Click OK
Connect each subsystem to the Bus Creator
If you Double click on the Bus Creator after connecting the subsystem you can view the input signals
Notes: Needs update

## Slide 50: High Level
Notes: Needs update

## Slide 51: High Level
Connect the output of the Bus Creator to each of the subsystem inputs
Rename the output signal of the Bus Creator to System_Signals
Notes: Needs update

## Slide 52: High Level
Notes: Needs update

## Slide 53: High Level
Congratulations! You have
  Created a high level hierarchical system
  Established communication between the three key subsystems
  Gained experience with Simulink
Notes: Needs update

## Slide 54: MBSD Lecture 2
Simple Vehicle Model

## Slide 55: Lecture Goals
Create the Vehicle subsystem
Create the MGA subsystem with a preposterous motor model
Observe and assess the results
Notes: Needs update

## Slide 56: Simple Vehicle
Save your previous model (Series_Hybrid_le1_a.slx) as Series_Hybrid_le2_a
In the Model Browser window, click on the Plant subsystem
Move the buses to the bottom of the window
Notes: Needs update

## Slide 57: Simple Vehicle
Notes: Needs update

## Slide 58: Simple Vehicle
Drag two Subsystems into the Plant window
Rename them
  Vehicle
  MGA
Right click on the Vehicle subsystem
  Select Rotate & Flip
  Flip Block Name
Repeat for the MGA subsystem
Notes: Needs update

## Slide 59: Simple Vehicle
Notes: Needs update

## Slide 60: Simple Vehicle
Let’s also color code our subsystems to make things easy to identify
  Right click on the subsystem
  Format/Background Color
Make the vehicle gray and MGA red
Notes: Needs update

## Slide 61: Simple Vehicle
Click to show hierarchical subsystems
Notes: Needs update

## Slide 62: Vehicle Subsystem
The Vehicle subsystem will mechanically receive torque via a shaft from MGA
We will skip mechanical brakes and use exclusively regenerative braking as applied by MGA
The Vehicle subsystem will contain
  Posi-trac rear axle
  Rear tires
  Vehicle solver
  Inertias for the driveshaft and axle half shafts
Notes: Needs update

## Slide 63: Vehicle Subsystem
Delete the In1 and Out1 blocks as well as the connecting wire
Copy the In1, Out1, Bus, Terminator, and Ground blocks from the Plant subsystem
Rename Plant to Vehicle
From
  Simscape / Utilities
Drag in a Connection Port and rename it Vehicle Mechanical Port
Notes: Needs update

## Slide 64: Vehicle Subsystem
From
  Simscape / Driveline / Tires & Vehicles
Drag in the Vehicle Body and one Tire(Magic Formula) blocks
From
  Simscape / Driveline / Gears
Drag in a Simple Gear block
Notes: Needs update

## Slide 65: Vehicle Subsystem
Notes: Needs update

## Slide 66: Vehicle Subsystem
Double click on the Simple Gear
We can specify the gear ratio and relative rotational directions
  Change the output shaft rotation to the same direction as input shaft
  Leave the ratio as 2
Notes: Needs update

## Slide 67: Vehicle Subsystem
Double click on the Tire block
  This block converts the applied torque to force in the x-direction
  It also determined whether or not the tire slips
  Keep the default values
Notes: Needs update

## Slide 68: Vehicle Subsystem
Double click on the Vehicle Body block
  This block solves linear momentum (with drag and pitch) from the tire force
  Keep the default values
Notes: Needs update

## Slide 69: Vehicle Subsystem
Connect the Vehicle Mechanical Port to the Base side of the Simple Gear
Connect the Follower side of the Simple Gear to the A port on the Tire
We now have a model of the driveshaft, rear differential, and axle shaft
Notes: Needs update

## Slide 70: Vehicle Subsystem
Driveshaft
Rear Diff
Rear Axle
Notes: Needs update

## Slide 71: Vehicle Subsystem
Note the difference in between the Driveline connection ports and the Simulink connection ports
They will not connect to each other
Driveline blocks are used to solve the Conservation of Angular Momentum principle during each time step
Notes: Needs update

## Slide 72: Vehicle Subsystem
Every shaft must have a mass moment of inertia
Also, a special solver must be used
From
  Simscape / Foundation Library / Mechanical / Rotational Elements
Drag in two Inertia blocks
From
  Simscape / Utilities
Drag in a Solver Configuration block
Notes: Needs update

## Slide 73: Vehicle Subsystem
Notes: Needs update

## Slide 74: Vehicle Subsystem
Connect the Inertias to the driveshaft and rear axle and Rename them:
  Driveshaft Inertia (kg m^2)
  Driver Halfshaft Inertia (kg m^2)
Connect the Solver Configuration to the driveshaft
Hide its name
Rename the Tire to Driver Tire
Rename the Simple Gear to Rear Diff
Notes: Needs update

## Slide 75: Vehicle Subsystem
Notes: Needs update

## Slide 76: Vehicle Subsystem
Rename and save you your model as Series_Hybrid_le2_b
Now we can connect the H port of the Drive Tire block to the H port of the Vehicle Body block
From
  Simscape / Utilities
Drag in two Simulink-PS Converter blocks
These blocks transfer Simulink signals to physical signals
Drag in two Ground blocks
Hide their names
Connect the Ground blocks to the Simulink-PS Converters
Connect the Simulink-PS Converters to the beta and W ports of the Vehicle Body block
Notes: Needs update

## Slide 77: Vehicle Subsystem
Notes: Needs update

## Slide 78: Vehicle Subsystem
The NR port of the Vehicle Body block is a physical signal reporting the normal force applied on the rear wheels
Connect the NR port of the Vehicle Body block to the N port of the Driver Tire block
Rearrange the block and wire to make model look good
S port of the Drive Tire block is a physical signal reporting tire slip
Notes: Needs update

## Slide 79: Vehicle Subsystem
Notes: Needs update

## Slide 80: Vehicle Subsystem
S port of the Drive Tire block is a physical signal reporting tire slip
NF port of the Vehicle Body block reports the normal load on the front tires
We are not interested in tire slip or the normal force on the front tire (this is a rear wheel vehicle)
From
  Simscape / Utilities
Grab two PS-Simulink Converter blocks (opposite of Simulink-PS Converter)
Grab two Terminator blocks
Hide name of PS-Simulink Converter and Terminator both blocks
Connect the PS-Simulink Converter blocks to the Terminators
Connect the S port of the Drive Tire block and NF port of the Vehicle Body block to the PS-Simulink Converter blocks
Rearrange the block to make the model look good and compact
Notes: Needs update

## Slide 81: Vehicle Subsystem
It is preferred for the wires not to cross as much as possible. You should place your blocks in position to avoid the wire crossing as much as possible
Notes: Needs update

## Slide 82: Vehicle Subsystem
Notes: Needs update

## Slide 83: Vehicle Subsystem
We need to send the vehicle velocity signal (from the V port of the Vehicle Body block) to other parts of the model
Grab a PS-Simulink Converter block and connect the V port of the Vehicle Body block to the PS-Simulink Converter
From
  Simulink / Signal Routing
Grab a Goto block
Connect the PS-Simulink Converter to the Goto block
Notes: Needs update

## Slide 84: Vehicle Subsystem
Double click on the Goto block and change the tag to Vehicle_Speed_ms
Make sure the visibility is set to local
Click OK
Drag the sides of the Goto block to make the name visible
Hide the name of Goto and PS-Simulink Converter blocks
Notes: Needs update

## Slide 85: Vehicle Subsystem
Notes: Needs update

## Slide 86: Vehicle Subsystem
From
  Simulink / Signal Routing
Grab a From block
Double click on the From block
Open the Goto tag bar and select Vehicle_Speed_ms
  Note: if you don’t see Vehicle_Speed_ms, click on Update Tags and try again
Click OK
Hide the name of the From block
Notes: Needs update

## Slide 87: Vehicle Subsystem
From
Goto
Notes: Needs update

## Slide 88: Vehicle Subsystem
Congratulations – you have a model of a vehicle that will (hopefully) move when subjected to a torque
From a vehicle diagnostics perspective, we are interested in two things
  Speed (mph)
  Distance Traveled (miles)
Move the Vehicle_Speed_ms From block down near the Vehicle Diagnostics Bus
From
  Simulink / Commonly Used Blocks
Drag in two Gain blocks and one Integrator block
Hide the name of the Integrator block
Notes: Needs update

## Slide 89: Vehicle Subsystem
Congratulations – you have a model of a vehicle that will (hopefully) move when subjected to a torque
From a vehicle diagnostics perspective, we are interested in two things
  Speed (mph)
  Distance Traveled (miles)
Move the Vehicle_Speed_ms From block down near the Vehicle Diagnostics Bus
From
  Simulink / Commonly Used Blocks
Drag in two Gain blocks and one Integrator block
Hide the name of the Integrator block
Notes: Needs update

## Slide 90: Vehicle Subsystem
Set the first Gain to 2.2374 (m/s to mph)
Set the second Gain to 6.214 e-4 (m/s to miles/s)
Name them accordingly
Connect the output of the From block to the input of the Gain blocks
Connect the second Gain block to the Integrator block
Delete the Grounds going into the Bus
Connect the two signals
Name them: (Double click on the wires)
  Vehicle_Speed_mph
  Vehicle_Distance_miles
Notes: Needs update

## Slide 91: Vehicle Subsystem
The Vehicle subsystem is done
  Note that we did not use any of the system signals
  When we get around to mechanical brakes we will need a brake signal
Take some time to move things around and make it look nice
Notes: Needs update

## Slide 92: Vehicle Subsystem
Notes: Needs update

## Slide 93: MGA Subsystem
Our motor model is going to be preposterously simple
  Constant torque output
  No RPM limits
  No input power required
Rename and save you model as:
  Series_Hybrid_le2_c
Use the Model Browser to go to the MGA subsystem
Notes: Needs update

## Slide 94: MGA Subsystem
Delete the In1, Out1, and the connecting wire
Copy the Bus from the Plant subsystem
  Rename accordingly
Drag in a Constant block and rename it MGA Max Torque (Nm)
Set the constant value at 200 Nm
From
  Simscape / Foundation Library / Mechanical / Mechanical Sources
Drag in an Ideal Torque Source block and hide its name
Drag in a Connection Port and rename it MGA Mechanical Port
Drag in a Simulink-PS Converter and hide its name
From
  Simscape / Foundation Library / Mechanical / Rotational Elements
Grab a Mechanical Rotational Reference block and hide its name
Wire everything together as shown in the next page
Notes: Needs update

## Slide 95: MGA Subsystem
Notes: Needs update

## Slide 96: MGA Subsystem
The only MGA diagnostic is the torque
Delete the Terminators
Double click on the Bus Creator and change the Number of inputs to 1
Click OK
Notes: Needs update

## Slide 97: MGA Subsystem
Drag in a pair of Goto and From blocks
Name them accordingly
Use them to route the MGA torque signal to the Bus Creator block
Name the signal going into the Bus
Compare with next slides
Notes: Needs update

## Slide 98: MGA Subsystem
Notes: Needs update

## Slide 99: MGA Subsystem
Congratulations – you’ve made a motor model
It is now time to connect MGA to the Vehicle and see what happens
Save your model as
  Series_Hybrid_le2_d
Use the Model Browser to go to the Plant level of the model
Make the MGA and Vehicle subsystems larger
Notes: Needs update

## Slide 100: Plant Level
Notes: Needs update

## Slide 101: Plant Level
The MGA Mechanical Port is on the wrong side of the block
Go into the MGA subsystem and double click on the Port
Change the location from left to right
Click OK
Notes: Needs update

## Slide 102: Plant Level
Connect the two Mechanical Ports
Route the Vehicle and MGA Diagnostics to the Plant Signal CAN Bus
  Name the signal inputs accordingly
Change the foreground of the Vehicle routing blocks to gray
Change the foreground of the MGA routing blocks to red
Notes: Needs update

## Slide 103: Plant Level
Notes: Needs update

## Slide 104: Plant Level
All that is left is to route the System Signals to the Vehicle and MGA
Delete the Terminators and the Bus Selector
Use the Goto and From blocks to route the System Signals to MGA and the Vehicle
Notes: Needs update

## Slide 105: Plant Level
Notes: Needs update

## Slide 106: Running the Model
It is now time to run the model
Go to the Vehicle subsystem
From
  Simulink / Sinks
Drag in a Scope
Connect it to the Vehicle_Speed_mph signal
Click on the Run button to start the simulation
Notes: Needs update

## Slide 107: Running the Model
Run
Notes: Needs update

## Slide 108: Running the Model
Oh! There is an error
Notes: Needs update

## Slide 109: Running the Model
Since we do not yet need any signals from the System Diagnostics bus, replace the Bus Selector with a Terminator in the
  Driver
  Controller
  Plant / Vehicle
  Plant / MGA
subsystems
Notes: Needs update

## Slide 110: Running the Model
Rerun the model
If the scope is not open, double click on the block
Observe the results
  0 to 25 mph in 10 seconds
You can check the results by hand
Gear ratio
Tire radius
Notes: Needs update

## Slide 111: Simple Vehicle
Review
  Vehicle subsystem
    Receives torque from MGA
    Solves vehicle velocity
    Sends/Receives CAN messages
  MGA subsystem
    Provides torque to Vehicle
    Sends/Receives CAN messages
Notes: Needs update

## Slide 112: MBSD Lecture 3
Initialization, Solver, Logging & Visualization, and Driver

## Slide 113: Lecture Goals
Create an initialization file for data management
Select the correct ODE solver
Create a Data Logging and Visualization subsystem
Create a Driver subsystem
Have the vehicle follow a drive cycle
Experiment with feedback gain
Notes: Needs update

## Slide 114: Initialization File
Save your previous model as
  Series_Hybrid_le3_a
Go to the System Level of the model
Right click on any vacant white space on the model
  Select Model Properties
  Select the Callbacks tab
  Click on the InitFcn
  Type Vehicle_Init_File_L3 in the second column
Notes: Needs update

## Slide 115: Initialization File
Notes: Needs update

## Slide 116: Initialization File
This is going to be a Matlab M-file which will automatically execute each time the model is run
All of our component parameters will go in this file
Start by going to the Matlab window
Open file
  Vehicle_Init_File_L3.m
Notes: Needs update

## Slide 117: Initialization File
Notes: Needs update

## Slide 118: Initialization File
We will replace the numeric values in the blocks with these variable names
  This consolidates all key parameters into one location
  Help prevent making mistakes
  Tip: copy the variable names from the M-file and paste into the block to prevent spelling errors
Update all relevant blocks
Notes: Needs update

## Slide 119: Initialization File
Notes: Needs update

## Slide 120: ODE Solver
While the Solver Configuration calls the hooks for solving the driveline angular momentum, an overall ODE solver must be specified
Our model contains a set of stiff ODEs and as recommended by The MathWorks, best solver suited for this type of ODEs is ODE23t
Notes: Needs update

## Slide 121: ODE Solver
As with the Init file, right click on the model background
Select
  Model Configuration Parameters
  Solver: ode23t (mod. stiff/Trapezoidal)
  Click OK
Run the model and note how much faster it runs!
Notes: Needs update

## Slide 122: ODE Solver
Notes: Needs update

## Slide 123: Logging & Visualization
Let’s now create a subsystem to represent the on-board data logger
This will also be a good place for having all the visualization
First, go to the Vehicle subsystem and delete the Scope block
  Having scopes in the model is bad for auto-code generation
Notes: Needs update

## Slide 124: Logging & Visualization
Drag a new Subsystem into the Plant level of the model
Rename it Logging & Visualization
Rename the In1 block to System Signals
Delete the Out1 block
  The logger does not send any diagnostics
Drag a Bus Selector into the subsystem
Go back into the Plant level of the model
Copy a System Signals From block and connect it to System Signals of Logging & Visualization subsystem
Notes: Needs update

## Slide 125: Logging & Visualization
Notes: Needs update

## Slide 126: Logging & Visualization
Notes: Needs update

## Slide 127: Logging & Visualization
In the Logging & Visualization subsystem
Double click on the Bus Selector block
In the Selected signals column
  Click on signal1 and then Remove
  Click on signal1 and then Remove
In the Signals in the bus column
  Click on Driver_Diagnostics and then Select
  Click on Plant_Diagnostics and then Select
  Click on Controller_Diagnostics and then select
Click OK
Notes: Needs update

## Slide 128: Logging & Visualization
Notes: Needs update

## Slide 129: Logging & Visualization
Drag in three Goto blocks and name them Driver_Diagnostics, Plant_Diagnostics, and Controller_Signals
Wire them to the Bus Selector
Drag in three From blocks
Terminate the Driver_Diagnostics and the Controller_Signals From blocks
Drag in a Bus Selector and wire it to the Plant_Diagnostics From block
Notes: Needs update

## Slide 130: Logging & Visualization
Double click on the Bus Selector
Remove signal1 and signal2
Select the Vehicle_Diagnostics and the MGA_Diagnostics signals
Drag in two more Goto blocks
  Connect them to the Bus Selector
  Name them accordingly
  Color them accordingly
Notes: Needs update

## Slide 131: Logging & Visualization
Notes: Needs update

## Slide 132: Logging & Visualization
Drag in two more From and Bus Selector blocks
Select
  Vehicle_Diagnostics - first From block
  MGA_Diagnostics – second From block
Connect the From blocks to the Bus Selector blocks
Use the Bus Selector blocks to select all signals
Notes: Needs update

## Slide 133: Logging & Visualization
One Signal
Two Signals
Notes: Needs update

## Slide 134: Logging & Visualization
From
  Simulink / Sinks
Drag in a To Workspace block
  This will write the desired signal values to an array for review when the simulation is done
Double click on the To Workspace block
  Make the following changes
    Variable name - Vehicle_Speed_mph
    Sample time - Logging_Sample_Time_s
    Save format – Array
Update the input file
Notes: Needs update

## Slide 135: Logging & Visualization
Very important: Don’t forget this
Notes: Needs update

## Slide 136: Logging & Visualization
Connect the To Workspace block to the Bus Selector
Repeat for the remaining signals coming from the Plant
Color everything accordingly
Notes: Needs update

## Slide 137: Logging & Visualization
Notes: Needs update

## Slide 138: Logging & Visualization
Rather than using Scope blocks, we will use the Signal and Scope Manager to view the signals
Right click on the Vehicle_Speed_mph signal and select
  Create & Connect Viewer / Simulink / Scope
Notes: Needs update

## Slide 139: Logging & Visualization
Notes: Needs update

## Slide 140: Logging & Visualization
Note the scope figure on the Vehicle_Speed_mph signal – that denotes that the signal is being scoped
Scope figure
Notes: Needs update

## Slide 141: Driver Subsystem
The Driver subsystem will be our first proportional feedback loop
  The vehicle will be at a certain speed
  The driver will want to go a different speed
  The driver will send a torque request (-1 to 1) to the controller
  The vehicle will change speed
  Repeat for the duration of the drive cycle
Notes: Needs update

## Slide 142: Driver Subsystem
Save the model as Series_Hybrid_le3_b
Use the Model Browser to go into the established Driver subsystem
Drag in a Bus Selector, a Goto, and a From block
Delete the Terminator and connect the Bus Selector block
Select the Vehicle_Speed_mph signal
Connect this signal to the Goto block
Notes: Needs update

## Slide 143: Driver Subsystem
Notes: Needs update

## Slide 144: Driver Subsystem
The drive cycle will be read in from the workspace
  It will contain time (s) and desired speed (mph) at that time
  We will use the standard FU505 drive cycle
    505 seconds long
    Collected data
  The data is stored as a .mat file
  The .mat file will be loaded with the init file
Notes: Needs update

## Slide 145: Driver Subsystem
From
  Simulink / Sources
Drag in a From Workspace block
  Double click on it
  Rename the Data to: Sch_Cycle
  Click OK
Notes: Needs update

## Slide 146: Driver Subsystem
Notes: Needs update

## Slide 147: Driver Subsystem
From
  Simulink / Commonly Used Blocks
Drag in a Sum, Gain, and Saturation block
  Make the Sum block rectangular with a +-
Drag in another two Goto and From blocks
Arrange, wire, and name as shown on the next slide
Notes: Needs update

## Slide 148: Driver Subsystem
Driver_Speed_Desired_mph
Driver_Torque_Request
Notes: Needs update

## Slide 149: Driver Subsystem
We must now determine the value of the error amplifier
Classical controls theory would have us generate a transfer function and look for poles
This system will soon become so complex that classic approaches do not work
Instead use some experience
If you are driving a car and want to go
  1 mph faster
  10 mph faster
  20 mph faster
You step on the gas (torque request)
  Very little
  Half way
  To the floor
Notes: Needs update

## Slide 150: Driver Subsystem
The torque request will vary from
  +1
    full positive torque requested
    20 mph+ too slow
  -1
    Full negative torque requested
    20 mph+ too fast
A gain of 0.05 will send a 1 at 20 mph error
A Saturation will limit the request to 1
Notes: Needs update

## Slide 151: Driver Subsystem
Notes: Needs update

## Slide 152: Driver Subsystem
The final step in the Driver subsystem is to add the desired drive cycle to the initialization file
Notes: Needs update

## Slide 153: Driver Subsystem
Run the init file manually to load the drive cycle
At the Matlab command line type
  plot(Sch_Cycle(:,1),Sch_Cycle(:,2))
Notes: Needs update

## Slide 154: Controller Subsystem
The Driver torque request will next be sent through the CAN bus to the Controller subsystem
Go to the Controller subsystem, delete the Terminators and Grounds, and drag in a Gain, a Bus Selector, two Goto, and two From blocks
On the Bus Selector, select the Driver_Torque_Request signal
Wire and label as shown on the next slide
Notes: Needs update

## Slide 155: Controller Subsystem
mga_torque_request
Notes: Needs update

## Slide 156: Controller Subsystem
The driver torque request passes through the controller where it is sent to MGA
  Just like a real vehicle
The Gain block can be modified
  Sporty : increase request
  Economy : decrease request
Naming convention
  All Control signals will be lowercase
  End with either “request” or “enable”
Notes: Needs update

## Slide 157: MGA Subsystem
The last step is to pass the torque request to MGA
Drag in a Bus Selector, a Goto, a From, and a Product block
Delete the Terminator
Select the mga_torque_request signal
Wire and label as shown on the next slide
Notes: Needs update

## Slide 158: MGA Subsystem
Notes: Needs update

## Slide 159: Run the simulation
Go to the model level and Run the model
Notes: Needs update

## Slide 160: Results
Run the model and observe the scope
It only ran for 10 seconds
Notes: Needs update

## Slide 161: Results
Open the Configuration Parameters
Change the Stop Time to
  Sch_Cycle(end,1)
Notes: Needs update

## Slide 162: Results
Run the simulation again
Awesome! The vehicle is doing something!
Note: in the Scope, go to Tools / Axes Scaling
Select: Automatically Scale Axis Limits
But How well?
Notes: Needs update

## Slide 163: Logging & Visualization
Go to the Logging & Visualization subsystem
Delete the Terminator on the Driver_Diagnostics From block
Use a Bus Selector to extract all Driver signals
Drag in two To Workspace blocks to log the Driver Data
Repeat for the Controller Signals
Notes: Needs update

## Slide 164: Logging & Visualization
Notes: Needs update

## Slide 165: Logging & Visualization
Right click on the Driver_Speed_Desired_mph signal
Select
  Connect to Existing Viewer
  Scope
Rerun the simulation and observe the scope
Notes: Needs update

## Slide 166: Logging & Visualization
Notes: Needs update

## Slide 167: Results
Our vehicle does a poor job of following the drive cycle
Increase the MGA max torque in the init file until the traces are similar
Blue trace
Yellow trace
Notes: Needs update

## Slide 168: Results
Even with 1000 Nm, the vehicle still can not follow the trace exactly
Put the torque back to 200 Nm
Notes: Needs update

## Slide 169: Results
Let’s see what the driver is doing
On the scope
Select
  View / Layout
Choose a 2×1 layout
Now we can add signals to both Axis 1 and Axis 2
Notes: Needs update

## Slide 170: Results
In the Logging & Visualization subsystem
  Right click on the Driver_Torque_Request signal
  Select
    Connect to Viewer / Scope / Axes 2
This will put the Driver torque request directly below the drive cycle
Rerun the simulation
Notes: Needs update

## Slide 171: Results
Wow – the driver torque request never goes above about 0.7
Why?
Notes: Needs update

## Slide 172: Results
Note that the vehicle is “chasing” a velocity and only occasionally off by more than 10 mph
Change the error amplifier in the Driver subsystem to make the driver more aggressive
Increasing the gain
  Decreases the proportional error
  Allows the system to respond faster
  Can cause overshoot and oscillations
Notes: Needs update

## Slide 173: Results
An error amplifier of 1 should work quite well
Notes: Needs update

## Slide 174: Results
As we expected, error amplifier of 1 worked quite well for this drive cycle
What about for a different drive cycle?
Notes: Needs update

## Slide 175: Results
In the init file
  Change the drive cycle to Schedule_Boston_Cab.mat
  Increase the MGA torque to 1000 Nm
Rerun the simulation
Notes: Needs update

## Slide 176: Results
Definitely some overshoot
Notes: Needs update

## Slide 177: Results
In the init file
  Change the drive cycle back to the FU505
  Change the MGA torque back to 200 Nm
In the Driver subsystem
  Change the error amplifier to 0.5
Rerun the simulation
Notes: Needs update

## Slide 178: Results
This provides a good balance of trace correlation and driver torque request
Notes: Needs update

## Slide 179: Initialization, Solver, and Driver
Review
  Created an initialization file to manage data
  Changed to appropriate ODE solver
  Created a logging and graphics subsystem
  Developed driver proportional feedback loop
    Velocity mismatch generates an error signal
    Error signal converted to a driver torque request
    Driver torque request goes to controller
    Controller requests MGA torque
  System response very sensitive to feedback gain value
Notes: Needs update

## Slide 180: MBSD Lecture 4
Improved MGA and Simple Battery

## Slide 181: Outline
Make MGA an ideal electromechanical device
Create a preposterous battery to power MGA
Track the battery state of charge (SOC)
Notes: Needs update

## Slide 182: MGA
Save your model as Series_Hybrid_le4_a.slx
Go into the MGA subsystem
MGA will still
  Have a constant maximum torque
  Have no rpm limits
  Be modulated by the Controller
By providing torque at a given RPM, power is transferred to the Vehicle
Notes: Needs update

## Slide 183: MGA
From
  Simscape / Foundation Library / Mechanical / Mechanical Sensors
Drag in an Ideal Rotational Motion Sensor block
From
  Simscape / Foundation Library / Mechanical / Rotational Elements
Drag in a Mechanical Rotational Reference block
Also drag in three Gotos, two Froms, two Gains, two PS-Simulink Converters, One Terminator and a Product block
Arrange and wire as shown on the next slide
Notes: Needs update

## Slide 184: MGA
Notes: Needs update

## Slide 185: MGA
Add the MGA_Speed_rpm and MGA_Mechanical_Power_kW to the MGA diagnostics bus
In the Logging & Visualization subsystem, extract and log these signals
Notes: Needs update

## Slide 186: MGA & Battery
To make the mechanical power, the motor will need to receive electrical power from the battery
This power will be the battery voltage times the current drawn
Let’s now add an ideal battery to the Plant
Drag in a Subsystem and rename it Battery
Make the background orange
Notes: Needs update

## Slide 187: Battery
The Battery will receive the system signals and broadcast its diagnostics
  Delete the wire connecting the In1 and Out1 blocks and rename them System Signals and Battery Diagnostics
  Terminate the System Signals
  Drag in a Bus Creator, connect it to the Battery Diagnostics, and ground the inputs
Notes: Needs update

## Slide 188: Battery
Electrically, the battery will
  Tell MGA its voltage
  Receive a current demand from MGA
From
  Simulink / Commonly Used Blocks
Drag in an In1 and an Out1 block
Rename them
  MGA Current Input (A)
  Battery Voltage Output (V)
Notes: Needs update

## Slide 189: Battery
Notes: Needs update

## Slide 190: Battery
For now, the battery voltage will be constant and defined in the init file
Drag in a Constant block
  Rename it Battery Voltage (V)
  Give it a variable name of Battery_Voltage
  Connect it to the Battery Voltage Output
Update the init file for the battery voltage to be 336V
Notes: Needs update

## Slide 191: Battery
Notes: Needs update

## Slide 192: Battery
Our magic battery can provide any amount of current required by the motor
Put the battery current and the battery voltage on the Battery Diagnostics bus
Notes: Needs update

## Slide 193: Battery
Notes: Needs update

## Slide 194: Battery
Outstanding, we now have a constant voltage power source with unlimited amperage and capacity
Return to the Plant level of the model
  Make the Battery subsystem larger
  Drag in three From and two Goto blocks
  Wire and label as shown on the next slide
Convention
  Physical signals get colored background
  CAN signals get colored foreground
Notes: Needs update

## Slide 195: Battery
Notes: Needs update

## Slide 196: Battery
Place the Battery Diagnostics onto the Plant CAN bus
Extract the Battery signals in the Logging & Visualization subsystem
Notes: Needs update

## Slide 197: MGA
Save the model as Series_Hybrid_le4_b.slx
In the MGA subsystem, drag in an In1 and Out1 block
Rename them
  Battery Voltage Input (V)
  MGA Current Output (A)
For now, the electrical power from the battery will equal the mechanical power from the motor
Notes: Needs update

## Slide 198: MGA
Thus the current required will be the mechanical power divided by the battery voltage
From
  Simulink / Math Operations
Drag in a Divide block
When MGA is drawing current, it will come out of the battery
Drag in a Gain block and give it a value of -1
Notes: Needs update

## Slide 199: MGA
Notes: Needs update

## Slide 200: MGA
Place the MGA Current signal onto the diagnostics bus
  Label it MGA_Current_A
Extract the signal in the Logging & Visualization subsystem
Notes: Needs update

## Slide 201: MGA / Logging & Visualization
Notes: Needs update

## Slide 202: MGA
Return to the Plant level of the model
Make the MGA subsystem larger
Use a Goto and a From block to connect MGA to the Battery
  Color accordingly
Notes: Needs update

## Slide 203: MGA
Notes: Needs update

## Slide 204: Logging & Visualization
Let’s now observe the MGA current as it follows the FU505 drive cycle
Go to the Logging & Visualization subsystem
  Add a third axis to the Scope
  Place the MGA_Current_A signal on the third axis
  Run the simulation
Notes: Needs update

## Slide 205: Results
Vehicle deceleration
Vehicle acceleration
Positive torque request
Negative torque request
Positive Current
Negative Current
Notes: Needs update

## Slide 206: Battery SOC
Let’s add battery charge to our model
Battery Capacity is in units of Amp hours
  The amount of charge transferred by a constant current of one amp for one hour
  Thus we can integrate the battery current to find out how much charge has been removed
This value can be non-dimensionalized by dividing by the maximum capacity of the battery to get the State of Charge (SOC)
  1 fully charged
  0 fully discharged
Notes: Needs update

## Slide 207: Battery SOC
In the Battery subsystem, drag in
  An Integrator block
  A Gain block
    1/3600
  Two Constant blocks
    Battery_Capacity 8.5 Ahrs
    Battery_Initial_SOC 0.7
  A Divide block
  And a Sum block
Arrange as shown on the next slide
Notes: Needs update

## Slide 208: Battery SOC
Notes: Needs update

## Slide 209: Battery SOC
Add the Battery_SOC signal to the Battery Diagnostics bus
Extract the signal in the Logging & Visualization subsystem
Right click on the Driver_Torque_Request signal
  Select Disconnect Viewer
  Select Scope
  Select Axes 2
Add the SOC signal to Axes 2
Notes: Needs update

## Slide 210: Logging & Visualization
Notes: Needs update

## Slide 211: Initialization
The last step is to add the two new battery parameters to the init file
Run the Simulation
Notes: Needs update

## Slide 212: Results
Vehicle accelerates
SOC Decreases
“Constant” high speed
Sharp drop in SOC
Vehicle decelerates
SOC Increases
Notes: Needs update

## Slide 213: Review
Developed an electromechanical model of MGA
  100% efficient
  Constant torque capable
  No rpm limits
Developed an electrical battery model
  100% efficient
  Constant voltage capable
  No current limits
  SOC ready
Notes: Needs update

## Slide 214: MBSD Lecture 5
Simple Charging logic

## Slide 215: Outline
Simple Battery charging
Simple GenSet charge logic
Notes: Needs update

## Slide 216: Battery SOC
While having our vehicle follow a drive cycle, the Battery SOC decreased
Eventually, the Battery SOC will get too low
  Permanent damage
  Stranded motorist
This will require an on-board power generating unit
  Diesel engine and MGB
Notes: Needs update

## Slide 217: Battery SOC / GenSet
The net effect of the GenSet is to provide power to the battery
  MGB current at Battery voltage
Let’s make a ridiculously simple MGB
  Constant current output
Rename the model Series_Hybrid_le5_a.slx
In the plant level of the model, drag in a new Subsystem and rename it MGB
  Make the background green
Notes: Needs update

## Slide 218: MGB
In the MGB subsystem
  Delete the connecting wire
  Create the System Signals and MGB Diagnostics bus
  Drag in a Constant block
    Rename it MGB Current (A)
    Give it a value of 5
  Drag in an Out1 block
    Rename it MGB Current Output (A)
  Put the current on the Diagnostics Bus
Notes: Needs update

## Slide 219: MGB
Notes: Needs update

## Slide 220: MGB
Return to the Plant level and put the MGB Diagnostics on the Plant Diagnostics Bus
Connect a System Signals From block
Go to the Logging & Visualization subsystem and extract the MGB diagnostics
Color accordingly!
Notes: Needs update

## Slide 221: MGB
Notes: Needs update

## Slide 222: MGB / Battery
Return to the Plant level of the model and use a Goto and a From block to make the electrical connection to the Battery
Notes: Needs update

## Slide 223: MGB / Battery
Notes: Needs update

## Slide 224: Battery
Drag in an In1 block and rename it MGB Current Input (A)
Drag in a Sum block and add the two Current Inputs together
Connect the output to the Battery_Current Goto block
Excellent – both MGs can remove/provide current from/to the Battery
Return to the Plant level and connect the MGB_Current_A From block
Notes: Needs update

## Slide 225: Battery
Notes: Needs update

## Slide 226: Battery
In the Logging & Visualization subsystem
  Right click on the Battery_SOC signal
  Create a new scope
  Give it three axis
    Axis 1 – Battery SOC
    Axis 2 – Battery Current
    Axis 3 – MGA and MGB Current
Run the simulation
Notes: Needs update

## Slide 227: Results
Notes: Needs update

## Slide 228: Results
The “trickle charge” of a constant 5 amps kept the SOC up but the Battery was still charge depleting
Vary the value of the MGB current until the Battery is relatively charge sustaining
Notes: Needs update

## Slide 229: Results
0.7 SOC
0.7 SOC
8 Amps
Notes: Needs update

## Slide 230: GenSet Controls
Our series electric vehicle will use a genset which will be activated intermittently
  SOC too low : start charging battery
  SOC too high : stop charging battery
Let’s make the idealized genset do exactly that via MGB and a state machine
Go to the Controller level of the model
Notes: Needs update

## Slide 231: GenSet Controls
From
  Simulink / Stateflow
Drag in a Chart block
  Rename it GenSet Controller
  Double click on it
The first logical state will be the “no charge” state
  The Battery SOC is above the lower limit
Notes: Needs update

## Slide 232: Stateflow
Left click on the State icon
Left click on the window
Name the state
  No_Charge
On entry, set the MGB charge enable to 0
Create a charge state
Notes: Needs update

## Slide 233: Stateflow
Notes: Needs update

## Slide 234: Stateflow
To go from one state to another, a transition must occur
These transitions are controlled by parameters called guards
If, at the instance the guard is queried, the parameters are true then the transition occurs
Let’s now create the transitions followed by the guards
Notes: Needs update

## Slide 235: Stateflow
Place the mouse over the No_Charge state
Left Click
Hold and drag to the Charge state
Connect the Charge back to the No_Charge
Notes: Needs update

## Slide 236: Stateflow
Left click on the right transition
Replace the question mark with the code at right
  Enclosed in square brackets
Repeat for the second transition
[Battery_SOC<battery_soc_low]
[Battery_SOC>=battery_soc_high]
Notes: Needs update

## Slide 237: Stateflow
Stateflow needs to know which state to “wake up” in
The default transition was created when the first state was placed
Default transition
Notes: Needs update

## Slide 238: Stateflow
We need to add the Battery_SOC input from Simulink into Stateflow
  Select
    Chart / Add Inputs & Outputs / Data Input From Simulink
  Change the Name to Battery_SOC
  Click OK
If you select
  Tools / Model Explorer
You can see that Battery_SOC has been added
Close Model Explorer
Notes: Needs update

## Slide 239: Stateflow
Notes: Needs update

## Slide 240: Stateflow
Similarly we need to add the value of mgb_charge_enable to Simulink
  Select
    Chart / Add Inputs & Outputs / Data Output to Simulink
  Change the Name to mgb_charge_enable
  Click OK
We also need to add the guards as parameters
  Select
    Chart / Add Other Elements / Parameter…
  Change the Name to battery_soc_low
  Click OK
Repeat for battery_soc_high
Notes: Needs update

## Slide 241: Stateflow
The final step is to set the frequency at which the guards are queried
  Select
    Chart / Add Inputs & Outputs / Event Input From Simulink
  Change the Name to Clock
  Click OK
After this step, Model Explorer should be as shown in the next slide
Notes: Needs update

## Slide 242: Model Explorer
Notes: Needs update

## Slide 243: GenSet Controller
Return to the Controller level of the model
Make the GenSet Controller subsystem larger
Extract the Battery_SOC from the System Signals bus and route it to the GenSet Controller
Route the mga_charge_enable signal to the Control Signals bus and add it
Notes: Needs update

## Slide 244: GenSet Controller
Notes: Needs update

## Slide 245: GenSet Controller
From
  Simulink / Sources
Drag in a Sine Wave block
  Rename it 10ms
Connect it to the Clock Port
Double Click on it
  Change the Frequency to 100*(2*pi)
  Click OK
Notes: Needs update

## Slide 246: GenSet Controller
Notes: Needs update

## Slide 247: GenSet Controller
Excellent, we have built a simple two state controller which, based on the Battery SOC, will determine whether or not it should be charged
This check will be performed every 10 ms
In the init file, we need to add guards
  Low SOC : 0.6
  High SOC : 0.7
Add to the init file
Notes: Needs update

## Slide 248: GenSet Controller
Notes: Needs update

## Slide 249: MGB
Return to the MGB subsystem
Extract the mgb_charge_enable signal from the System Signals
Drag in a Product block and multiply the mgb_charge_enable signal with the MGB Current block
Run the simulation
Notes: Needs update

## Slide 250: MGB
Notes: Needs update

## Slide 251: Results
SOC drops below 0.6
MGB starts charging
Notes: Needs update

## Slide 252: Results
In the init file, change the drive cycle to
  Schedule_FU505_Ten_Times.mat
Increase the MGB current to 50 amps
Run the simulation
  MGB now cycles on and off
  Watch the Stateflow chart
    The current state is highlighted during the simulation
Notes: Needs update

## Slide 253: Results: MGB not charging
Notes: Needs update

## Slide 254: Results: MGB charging
Notes: Needs update

## Slide 255: GenSet and Stateflow
Review
  Created a simple GenSet which provides current to recharge the battery
  Tweaked the trickle charge current for charge sustaining
  Created a state controller to turn the charge on and off
Notes: Needs update

## Slide 256: MBSD Lecture 6
Improved GenSet and Controls

## Slide 257: Outline
Improved MGB model
Simple diesel engine model
Charging logic
Notes: Needs update

## Slide 258: Improved GenSet
Previously, the GenSet simply provided a constant current
Improvements
  Diesel Engine
    Constant torque
    Speed control
  MGB
    Recycle MGA model
Rename your model
  Series_Hybrid_le6_a.slx
Notes: Needs update

## Slide 259: Improved MGB
Delete the MGB model you just got done making
Copy the MGA model
  Make it green
  Rename EVERYTHING from MGA to MGB
Add the MGB max torque to the init file
  200 Nm
Update the Logging & Visualization for MGB
  Note: We will create the signal for mgb_torque_request later in the controller subsystem
Notes: Needs update

## Slide 260: Improved MGB
We will make this signal later in the Controller
Notes: Needs update

## Slide 261: Logging & Visualization
Notes: Needs update

## Slide 262: Engine
Return to the Plant level, drag in a Subsystem, and rename it Engine
  Make it yellow
In the Engine subsystem, create the System Signals and Engine Diagnostics bus
Drag in a Connection Port for the mechanical connection to MGB
Notes: Needs update

## Slide 263: Engine
Notes: Needs update

## Slide 264: Engine
Drag in
  One Constant
  One Simulink-PS Converter
  One Ideal Torque Source
  One Inertia
  One Ideal Rotational Motion Sensor
  One Gain
  One Terminator
  One Product
  Two Goto
  Two PS-Simulink Converters
  Two Mechanical Rotational References
Arrange and label as shown on the next slide
Notes: Needs update

## Slide 265: Engine
Notes: Needs update

## Slide 266: Engine
Our engine torque will be modulated with a throttle request from the Controller
  Range of 0 to 1
  Analogous to a driver stepping on the accelerator pedal
Place the engine torque and speed on the Diagnostic bus
Notes: Needs update

## Slide 267: Engine
Notes: Needs update

## Slide 268: Engine
Return to the Plant level of the model
Connect a System Signals From block
Place the Engine Diagnostics on the CAN Bus
Connect the Engine mechanical port to the MGB mechanical port
Go to the Logging & Visualization and extract the Engine diagnostics
Notes: Needs update

## Slide 269: Engine
Notes: Needs update

## Slide 270: Logging & Visualization
Notes: Needs update

## Slide 271: Engine
Now place the Engine parameters into the init file
  Engine_Max_Torque = 200 Nm
  Engine_Inertia = 1.5e-3 kg m^2
Notes: Needs update

## Slide 272: Engine / Controller
To keep things simple
  No Charge State
    MGB charge enable = 0
    Engine throttle request = 0
  Charge State
    MGB charge enable = 1
    Engine throttle request = 0.5
Add the new engine throttle data to the Stateflow Controller
Place the engine throttle signal on the bus
Notes: Needs update

## Slide 273: Controller
Notes: Needs update

## Slide 274: Controller
Notes: Needs update

## Slide 275: Engine / GenSet
Return to the Engine subsystem and extract the throttle request signal
Excellent, the first pass Engine and associated improved GenSet is complete
Drag in a Solver Configuration block and connect the block as shown in the next slide
Notes: Needs update

## Slide 276: Engine
Notes: Needs update

## Slide 277: Controller
The controller will need to send a torque request to MGB to hold the engine at a constant desired speed
  Engine too fast – increase torque
  Engine too slow – decrease torque
Go to the Controller level of the model
Extract the engine speed signal
Notes: Needs update

## Slide 278: Controller
Notes: Needs update

## Slide 279: Controller
As done with the Driver subsystem
  The actual engine speed will be subtracted from the desired speed
  This will create an error signal
  The error signal will be amplified
  The amplified signal will be saturated
  The resulting torque request will be sent to MGB
Implement this feedback controller
Update the Control Signals bus
Notes: Needs update

## Slide 280: Controller
Give the Engine_Speed_Desired a value of 1800 in the init file
Saturate from 1 to -1
Multiply by mgb_charge_enable to “turn off” controller when not charging
Update
Notes: Needs update

## Slide 281: MGB and Visualization
Go to the MGB subsystem and extract the mgb_torque_request signal
Go to the Logging & Visualization subsystem
  Right click on the Vehicle_Speed_mph signal
  Open the Scope
  Add the MGB_Current_A signal to the third axis
  Create a fourth axis and put the Engine_Speed_RPM signal on it
Notes: Needs update

## Slide 282: Visualization
Create a new scope
  Axis 1 : Battery SOC
  Axis 2 : Engine Torque and MGB Torque
  Axis 3 : Engine Speed
Run the FU505 cycle to save time
Notes: Needs update

## Slide 283: Results
0.001 seconds to go from 0 to 1800 rpm
Notes: Needs update

## Slide 284: Improved GenSet & Controls
Review
  Made MGB a duplicate of MGA
  Created a very simple diesel engine
  Updated the controller to intermittently obtain current from the GenSet
Notes: Needs update

## Slide 285: Lectures 0 - 6
We built a model of a series electric vehicle
  Plant
  Driver
  Controller
All of the plant components are crude
  System response could be intuited
  Complex system was established
Component refinement is next
  Controller will need to be updated
Notes: Needs update

## Slide 286: Lectures 0 - 6
The high level plant model will not change!
Notes: Needs update

## Slide 287: Lectures 0 - 6
The Driver will not change!
Notes: Needs update

## Slide 288: Lectures 0 - 6
Driver torque request will not change
There will be a continuous feedback controller
The state controller will get more complicated!
More signals may be required and sent
Notes: Needs update

## Slide 289: MBSD Lecture 7
Improved Engine Model and MPGGE SOC Fuel Efficiency

## Slide 290: Outline
Improve Engine model
  Experimental data for torque curves
  Experimental data for fuel consumption
  Controller refinements
Fuel Efficiency
  Calculate MPG, MPGGE, and MPGGE with SOC correction
Notes: Needs update

## Slide 291: Experimental Data
Using the engine dynamometer at Rose-Hulman, a small diesel engine was tested at various engine speeds and throttle posititions
Data for torque (Nm) and fuel consumption (grams/sec) were collected
Let’s add this to our model
Rename your model
  Series_Hybrid_le7_a.slx
Notes: Needs update

## Slide 292: Experimental Data
In the Matlab Window, go to
  Current Directory window
  Double click on the Component_Data folder
At the command line, type
  clear variables
  load Engine_Diesel_Data
The loaded variables will appear in the Workspace window
Notes: Needs update

## Slide 293: Experimental Data
Notes: Needs update

## Slide 294: Experimental Data
Note the size of the matrices
  Engine_Fuel_Data : 15x21
  Engine_Fuel_RPM_Axis: 15x1
  Engine_Fuel_Throttle_Axis: 1x21
Thus
  The data rows are for given rpms
  The data columns are for given throttle positions
At the command line type
  surf(Engine_Fuel_Throttle_Axis, Engine_Fuel_RPM_Axis, Engine_Fuel_Data)
Notes: Needs update

## Slide 295: Experimental Data
Below idle, no fuel delivered
At zero throttle, no fuel delivered
Notes: Needs update

## Slide 296: Experimental Data
This engine does not have an idle circuit
  750 rpm is the lowest it can run
  A throttle signal of zero will send no fuel
  It will stall out
This is great!
  Our controller completely rules the throttle signal
Modify the previous surf command to view the torque data
Notes: Needs update

## Slide 297: Experimental Data
While cranking, the engine produces negative torque (friction and pump losses)
At zero rpm, the engine produces zero torque
At zero throttle, the engine produces negative torque
750 rpm is the lowest speed where torque can be produced
At higher rpm’s, insufficient fuel results in a negative torque
Notes: Needs update

## Slide 298: Engine
We will need to read in this data with a 2-d lookup table
Go to the Engine subsystem and delete the
  Engine_Max_Torque Constant
  engine_throttle_request From
  Product block
  Engine_Torque_Nm Goto
Notes: Needs update

## Slide 299: Engine
Notes: Needs update

## Slide 300: Engine
From
  Simulink / Lookup Tables
drag in two
  2-D Lookup Table blocks
Rename them
  Engine Torque (Nm)
  Engine Fuel Rate (grams/sec)
Notes: Needs update

## Slide 301: Engine
Notes: Needs update

## Slide 302: Engine
Double click on the Engine Torque table
In the dialogue box, change
  Table data: Engine_Torque_Data
  Breakpoints 1: Engine_Torque_RPM_Axis
  Breakpoints 2: Engine_Torque_Throttle_Axis
Click OK
Note the shape of the table
  It looks like the data!
Repeat for the Fuel Rate table
Notes: Needs update

## Slide 303: Engine
Notes: Needs update

## Slide 304: Engine
Double click on the Engine Torque table
Click the Edit table and breakpoints… button
  Note that all the data shows up
Click on the Mesh Plot icon
Verify that the shape is correct
  Easy to make a mistake, especially with square matrix data!
Close the mesh plot and the Editor
Click Cancel on the dialogue box
Notes: Needs update

## Slide 305: Engine
Mesh Plot
Engine Speed
Throttle request
Notes: Needs update

## Slide 306: Engine
Notes: Needs update

## Slide 307: Engine & Logging
In the Engine subsystem, route
  An engine rpm signal to each table
    Top input
  A throttle request signal to each table
    Bottom input
  The torque output to the Simulink-PS Converter
  The fuel rate output to the Engine Diagnostics bus
  Put a Goto block on the Engine Torque signal: Engine_Torque_Nm
In the Logging & Visualization subsystem
  Extract the engine fuel rate signal
Notes: Needs update

## Slide 308: Engine & Logging
Notes: Needs update

## Slide 309: Engine & Logging
Notes: Needs update

## Slide 310: Engine & Initialization
In the init file, add the line
  load Component_Data/Engine_Diesel_Data.mat
Update the engine inertia to 0.12
  The crankshaft and flywheel
Notes: Needs update

## Slide 311: Directory
Recall that we used the Matlab window to browse into the Component_Data directory
Matlab MUST be in the same working directory as the Simulink model
In the Matlab window
  Click on the Go up one level icon
Run the Simulink model
Notes: Needs update

## Slide 312: Results
The results look very similar to those previous
  The model still appears to be responding correctly
  At 1800 rpm and 0.5 throttle, the engine torque should be about 150 Nm
  Verify
Notes: Needs update

## Slide 313: Results
Notes: Needs update

## Slide 314: Results
Use the Zoom icon to zoom in on the time when the engine is starting
  261 seconds
Lets’s make a new scope for further investigation
Engine starts making torque at 750 rpm
MGB becomes generator near 1800 rpm
Torque appears negative while cranking
Notes: Needs update

## Slide 315: Results
For the new scope
  Axis 1
    Engine speed
  Axis 2
    Engine torque
    MGB torque
  Axis 3
    Engine fuel rate
Rerun the simulation
Fuel applied at 750 rpm
Notes: Needs update

## Slide 316: Results & Controller
We don’t want the engine to start making power until it is closer to the operating point
An additional logic state will be needed
  Set mgb_charge_enable to 1 to start engine
  Set engine_throttle_request to 0 until “close” to operating rpm
Then go into the Charge state
Notes: Needs update

## Slide 317: Controller
Go to the Controller subsystem
  Open the Stateflow GenSet Controller
  Add this new state
    Engine_Speed_RPM is a Simulink input
    Engine_Speed_Desired is a parameter
  What is a good value for “close” to 1800?
Notes: Needs update

## Slide 318: Controller
New Input
New parameter
Intermediate Engine_Ramp_Up state
1700 rpm sounds like a good rpm to engage the fueling
Notes: Needs update

## Slide 319: Controller
Notes: Needs update

## Slide 320: Controller
New Input
Notes: Needs update

## Slide 321: Results
X-axis zoom in on the engine ramp up
Y-axis zoom in on the engine speed
The fuel rate is about 90 rpm late
  Why?
Fuel should start flowing!
Fuel starts about 90 rpm late
Notes: Needs update

## Slide 322: Results
The ridiculous MGB starts the engine far too quickly
  The transition guards are checked every 10 ms
  In 10ms the engine speed goes from 1500 to almost 1800 rpm
  The transition point was almost missed!
Engine ramp-up rate will be addressed after we improve the MGB model
Notes: Needs update

## Slide 323: Results
X-axis zoom in on the engine coast down
Everything here looks fine
  Fuel shuts off
  Engine coasts down in about 4 seconds
Notes: Needs update

## Slide 324: MPG
Let’s now calculate the vehicle fuel efficiency
  MPG
  SOC correction
  GE (gas equivalent)
We will do this with a post-processing file
  Simply for experience
  Could be done in the Logging & Visualization subsystem
Notes: Needs update

## Slide 325: MPG
Calculating MPG is easy!
  Distance traveled / gallons consumed
We already have a signal for distance traveled in miles
We need a fuel consumed signal
  Add an Integrator into the Engine subsystem to calculate the amount of fuel consumed in grams
  Add the signal to the Engine Diagnostics bus
  Extract it in the Logging & Visualization
All of the remaining calculations are done in post file
Notes: Needs update

## Slide 326: Engine & Logging
Notes: Needs update

## Slide 327: SOC
If we removed energy from the battery during the drive cycle, we must calculate the additional amount of fuel required to replace it
If we added energy to the battery, we must calculate the amount of fuel required to produce that energy and subtract the fuel from our total
Notes: Needs update

## Slide 328: SOC
Step 1 – Amp Hours Consumed
  Ah_Consumed = (Initial_SOC – Final_SOC) * Battery_Capacity
    Battery capacity is in Ah (8.5 Ah for our model)
Step 2 – Convert to Energy
  Electrical_Energy = Ah_Consumed * Battery_OCV
    OCV (open circuit voltage) is determined experimentally from V-I plots (366 V in our model) and changes with the SOC. Energy is in Watt-hr.
Notes: Needs update

## Slide 329: SOC
Step 3 – Conversion Efficiency
  Electrical_Energy_BTU = (3.412*Electrical_Energy) / Efficiency
    Conversion efficiency is also determined experimentally by ANL (25% approximation generous)
    The 3.412 converts Watt-hr to BTU
Excellent – we now know the energy in BTU needed to account for the charge added to or removed from the battery
Notes: Needs update

## Slide 330: MPGGE
As a standard for comparison, we employ the MPGGE with SOC correction
This gives the equivalent amount of RFG required to produce the same energy used in the drive cycle
We already know the BTUs of energy needed to correct the SOC
Notes: Needs update

## Slide 331: MPGGE
Step 4 – Fuel Energy BTU
  Fuel_Energy_BTU = Fuel_Consumed_Gallons* 133393.1102
Step 5 – Total Energy BTU
  Total_Energy_BTU = Electrical_Energy_BTU + Fuel_Energy_BTU
133393.1102 BTU/Gal is the fuel heating value of B-20
Excellent – we now know the total energy consumed by our vehicle over the drive cycle
Notes: Needs update

## Slide 332: MPGGE
Step 6 – RFG Required
  Fuel_Consumed_RFG = Total_Energy_BTU / 114871.7446
    This gives us the gallons of RFG required to produce the same energy
    114871.7446 BTU/gal is the fuel heating value of RFG
Step 7 – MPGGE with SOC Correction
  MPGGE = Distance_Travelled / Fuel_Consumed_RFG
Notes: Needs update

## Slide 333: Vehicle_Post_File.m File
Notes: Needs update

## Slide 334: Post Processing File
Like the init file, the post file should run after every simulation
Right click on the model and
  Select Model Properties
  Select Callbacks
  Select StopFnc
  Enter the name of the post processing file without the .m
Notes: Needs update

## Slide 335: Results
Rerun the simulation
Not bad
  102 MPGGE w/SOC
  123 MPG straight
Unrealistic?
  100% regen braking
  100% efficient battery
  100% efficient MGs
We’ll watch there numbers go down!
Notes: Needs update

## Slide 336: Review
Improve Engine model
  Experimental data for torque curves
  Experimental data for fuel consumption
  Controller refinements
Fuel Efficiency
  Calculate MPG, MPGGE, and MPGGE with SOC correction
Notes: Needs update

## Slide 337: MBSD Lecture 8
Improved Battery Model

## Slide 338: Outline
Improve Battery model
  First order math model
    Variable battery voltage
  Algebraic loops
  Variable open circuit voltage
  Variable charge/discharge resistance
  Numeric error
Notes: Needs update

## Slide 339: Simple Battery
Thus far, the battery model
  Has had a constant voltage of 336V
  Has had a constant OCV of 366V
  Been able to provide infinite current
  Has had no energy conversion losses
Let’s now improve the battery model by including the internal resistance
  The battery voltage is now a function of the current
Notes: Needs update

## Slide 340: Battery Terminal Voltage
Current is defined as positive into the battery
Positive current charges the battery and increases the battery SOC
Notes: Needs update

## Slide 341: Future Improvements
For now, the open circuit voltage and the battery series resistance are a constant
As our understanding of the model increases, we can make the battery model less ideal by:
  Making a function of SOC and temperature
  Having a different charge and discharge series resistances, both of which are a function of SOC and temperature
These will all involve experimental (or manufacturer) data and 2-d lookup tables
Notes: Needs update

## Slide 342: First Order Model
The battery OCV and series resistance will be constants read from the init file
  Battery_OCV = 366
  Battery_Resistance = 0.4
Add to the init file
Remove the Battery_Voltage
Remove the OCV from the post file
Rename your model Series_Hybrid_le8_a.slx and implement the battery voltage equation
Notes: Needs update

## Slide 343: First Order Model
Notes: Needs update

## Slide 344: Results
Run the Simulation – Dooh!
Algebraic Loop: This means a variable is a function of itself!
Click here to go to the problem
Notes: Needs update

## Slide 345: Algebraic Loop
To calculate the MGB current ….
Notes: Needs update

## Slide 346: Algebraic Loop
Aha! The loop involves the battery voltage which is a function of the battery current which is a function of the battery voltage …
To break the algebraic loop a delay will be used to have either
  The battery voltage signal lag the battery current calculation or
  The battery current signal lag the battery voltage calculation
Close the Simulations Diagnostics box
Notes: Needs update

## Slide 347: Algebraic Loop
Go to the MGB subsystem where the algebraic loop was first identified
From
  Simulink / Discrete
Drag in a Memory block
Insert it just after the Voltage Input block
Thinking ahead, MGA is also used to calculate the battery current
Put a Memory block there too
Notes: Needs update

## Slide 348: MGA/MGB Voltage Delay
Notes: Needs update

## Slide 349: Results
Run the simulation and…
A value that is not finite means we are dividing by zero somewhere in the model … (Note that it occurs at time 0)
Click here to go to the Battery subsystem
Notes: Needs update

## Slide 350: Not finite (infinity)
The battery current is coming from : MGA and MGB current inputs
Notes: Needs update

## Slide 351: Not finite (infinity)
Dividing the Mechanical Power by the delayed Battery Voltage
Notes: Needs update

## Slide 352: Not finite (infinity)
At the start of the simulation (time zero), there is no delayed value of voltage
What does the memory block do?
  Double click on it
  Aha! It uses zero as its first value…
  which results in a divide by zero error at time zero
The first strategy of delaying the Battery voltage signal was a bad one
Undo the MGA/MGB improvements
Notes: Needs update

## Slide 353: Algebraic Loop
Let’s try strategy two, delaying the Battery current in calculating the Battery Voltage
Close the Simulation Diagnostics box
Close the MPGGE dialogue boxes
Go to the Battery subsystem
  Insert the Memory block into the Battery voltage calculation
  Verify that there are no downstream divides that could result in division by zero
Run the simulation
Notes: Needs update

## Slide 354: Results
Make new scope with Vehicle Speed, Battery Voltage, Battery current, MGA and MGB current
Battery Voltage is 366 when there is no battery current
Large voltage drop when MGB pulled large current to start engine
Notes: Needs update

## Slide 355: Results
Negative MGA current results in Negative Battery current
Negative Battery current results in Decreased Battery Voltage
Decreased Battery voltage results in Increased MGA current for torque request
Increased MGA current results in Faster reduction in Battery SOC
Faster Battery SOC reduction results in decreased MPGGE w/SOC correction
Notes: Needs update

## Slide 356: Results
This simple improvement has substantially decreased our SOC corrected MPGGE
Let’s improve the model further and see how the fuel economy is affected
First, we will add a variable OCV as a function of SOC and temperature
At the Matlab command line type
  clear variables
  load Component_Data/Battery_Data.mat;
  Click on the Workspace tab
Notes: Needs update

## Slide 357: Battery Data
Data matrix
Column vector
Row vector
Notes: Needs update

## Slide 358: Battery Data
At the command line, type
  surf(Battery_OCV_Temp_Axis, Battery_OCV_SOC_Axis, Battery_OCV_Data)
Repeat for the resistance data
OCV
Charge
Discharge
Notes: Needs update

## Slide 359: Battery Data
Add the loading of the battery data to the init file
Keep the constant value of OCV for the post file
Notes: Needs update

## Slide 360: Variable OCV
Save your model as
  Series_Hybrid_le8_b.slx
Go to the Battery subsystem
Delete the Battery OCV Constant block
Drag in a
  2-D Look up Table block
  Constant block
Add the OCV signal to the Battery Diagnostics Bus and extract it in the Logger
Notes: Needs update

## Slide 361: Variable OCV
Assume constant battery temperature
Notes: Needs update

## Slide 362: Variable OCV
Notes: Needs update

## Slide 363: Logging & Visualization
Notes: Needs update

## Slide 364: Variable OCV
We’ve got a lot of scopes – delete them all
Create a new one
  Axis 1 – Vehicle Speed (Desired & Actual)
  Axis 2 – Battery SOC
  Axis 3 – Battery, MGA, & MGB current
  Axis 4 – Battery OCV and Voltage
Run the simulation
Notes: Needs update

## Slide 365: Variable OCV
Better than before (higher end SOC)
Lower than before (Lower OCV)
Notes: Needs update

## Slide 366: Variable Internal Resistance
The internal resistance of the battery is also a function of the temperature and SOC
It also varies for charging and discharging
Drag in
  A Subsystem block
And rename it
  Battery Internal Resistance (Ohms)
Notes: Needs update

## Slide 367: Variable Internal Resistance
It will have three inputs
  Battery Current
  Battery SOC
  Battery Temperature
Add one output
  Battery Internal Resistance
Put the Battery Resistance on the Diagnostics Bus and extract it in the Logger
Notes: Needs update

## Slide 368: Variable Internal Resistance
Notes: Needs update

## Slide 369: Variable Internal Resistance
We will use the current to tell if we are charging or discharging
From
  Simulink / Commonly Used Blocks
Drag a Switch block into the Battery Resistance subsystem
Also drag in
  two 2-D Lookup Table blocks
  three Goto and five From blocks
Notes: Needs update

## Slide 370: Variable Internal Resistance
Notes: Needs update

## Slide 371: Variable Internal Resistance
When the current is positive (charging) the data from the top table is passed
Notes: Needs update

## Slide 372: Variable Internal Resistance
Put the resistance on a new scope and run the simulation
Notes: Needs update

## Slide 373: Results
Notes: Needs update

## Slide 374: Results
Higher internal resistance lowered the fuel economy
Run the FU505_Ten_Times.mat drive cycle
Notes: Needs update

## Slide 375: Results
Notes: Needs update

## Slide 376: Review
Improved the battery model
  Used first order model battery model to incorporate internal resistance, making battery voltage a function of battery current
  Discovered and corrected an algebraic loop with a memory block
  Improved the model with open circuit voltage data based on SOC and battery temperature
  Improved the model with variable charge and discharge internal resistances based on SOC and battery temperature
Notes: Needs update

## Slide 377: MBSD Lecture 9
Improved MG Model

## Slide 378: Outline
Improved Motor/Generator model
  Variable torque
  Constant conversion efficiency
  Variable conversion efficiency
Notes: Needs update

## Slide 379: MG Data
At the Matlab command line type
  clear variables
  load Component_Data/MG_Data.mat
Efficiency 2-D Lookup Table
Torque 1-D Lookup Table
Notes: Needs update

## Slide 380: Initialization
Add the MG data loading to the init file
Also add an MG inertia of 0.1 kg m^2
Notes: Needs update

## Slide 381: Variable Torque
We will start with the MGA subsystem
  Once we have it refined, we will copy it to MGB
Rename your model
  Series_Hybrid_le9_a.slx
Go to the MGA subsystem
  Change the name of all Goto and From blocks to MG
Notes: Needs update

## Slide 382: Variable Torque
Notes: Needs update

## Slide 383: Variable Torque
Drag in
  An Inertia block
  A 1-D Lookup Table block
Delete the MGA_Max_Torque block
Arrange as shown on the next slide
Add the
  MG_Torque_RPM_Axis
  MG_Torque_Data
to the Lookup Table
Notes: Needs update

## Slide 384: Variable Torque
Notes: Needs update

## Slide 385: Results
Let’s create a new scope
  Axis 1 – Vehicle speed (desired and actual)
  Axis 2 – Battery SOC
  Axis 3 – MGA Torque
  Axis 4 – MGA Speed rpm
Run the simulation for the FU505 drive cycle
Notes: Needs update

## Slide 386: Results
MGA max torque is a little more than before
MGA speed stays below about 1500 rpm
Notes: Needs update

## Slide 387: Efficiency
Electromechanical energy conversion can go two ways
  Electrical to mechanical
    Accelerating the vehicle
  Mechanical to Electrical
    Regenerative braking
This is a little more challenging than the battery efficiency
We will start by assuming a constant conversion efficiency of 0.85
Notes: Needs update

## Slide 388: Efficiency
Drag a Subsystem block into MGA and
Rename
  Subsystem to Conversion Efficiency
  In1 to Mechanical Power (W)
  Out1 to Electrical Power (W)
Add a Gain and a Goto for the Electrical Power
Notes: Needs update

## Slide 389: Efficiency
Notes: Needs update

## Slide 390: Efficiency
Go to the Conversion Efficiency subsystem
Drag in
  A Constant block
  A Switch block
  Two Product blocks
  A Goto block
  Two From blocks
Notes: Needs update

## Slide 391: Efficiency
If the mechanical power is positive
  Top of switch
  The motor is accelerating the vehicle
  A higher electrical power is required
  Therefore divide MP by the efficiency
If the mechanical power is negative
  Bottom of switch
  The generator is making power
  A lower electrical power is made
  Therefore multiply MP by the efficiency
Arrange as shown on the next slide
Notes: Needs update

## Slide 392: Efficiency
Notes: Needs update

## Slide 393: Efficiency
Add the Electrical Power to the Diagnostics bus
Extract it in the Logging & Visualization subsystem
Create a scope
  Axis 1 – Vehicle Speed (actual)
  Axis 2 – Mechanical and Electrical Power
Notes: Needs update

## Slide 394: Results
Wow! Large drop in efficiency
Mechanical Power exceeds Electrical Power
Notes: Needs update

## Slide 395: Variable Efficiency
Conversion efficiency is a function of both MG speed and current
Let’s add that in
Rename you model
  Series_Hybrid_le9_b.slx
In the Conversion Efficiency subsystem
  Delete the Efficiency block and Goto/From blocks
Notes: Needs update

## Slide 396: Variable Efficiency
Drag in
  Two 2-D Lookup Table blocks
  Two In1 blocks
  Two Goto blocks
  Four From blocks
Arrange and label as shown on the next slide
Notes: Needs update

## Slide 397: Variable Efficiency
Notes: Needs update

## Slide 398: Variable Efficiency
Notes: Needs update

## Slide 399: Variable Efficiency
Hmmm, our efficiency data is for positive values of current and MG speed
  Can either of these be negative?
From
  Simulink / Math Operations
Drag in two Absolute Value blocks
Return to the MGA subsystem
  Connect the necessary From blocks
Run the simulation
Notes: Needs update

## Slide 400: Variable Efficiency
Notes: Needs update

## Slide 401: Variable Efficiency
Notes: Needs update

## Slide 402: Variable Efficiency
Behaving as expected
Slight Improvement
Notes: Needs update

## Slide 403: Variable Efficiency
Outstanding, we now have a pretty good model of a motor/generator
Go to the Plant level of the model
  Delete MGB
  Copy MGA
  Update the names accordingly
Extract the MGB electrical power in the Logging & Visualization subsystem
Notes: Needs update

## Slide 404: MGB
Notes: Needs update

## Slide 405: Results
One last new scope
  Axis 1 – Vehicle speed (actual and desired)
  Axis 2 – SOC
  Axis 3 – Battery, MGA, & MGB current
  Axis 4 – Engine rpm
Run the Simulation
Notes: Needs update

## Slide 406: Results
Looks like our improved MGB really broke something
Notes: Needs update

## Slide 407: Results
Aha – our desired engine speed is 1800 rpm
  Engine torque at 0.5 throttle 145 Nm
  MGB max torque 140 Nm
MGB can’t control the engine!
Decrease the desired engine speed to 1500 rpm
Notes: Needs update

## Slide 408: Results
Much better
Notes: Needs update

## Slide 409: Review
Improved MG Model
  Variable maximum torque wrt MG speed
  Constant efficiency to explore electromechanical conversion losses
  Variable efficient wrt MG speed and current
Notes: Needs update

## Slide 410: Future Direction
We blew up our battery
  Need to add current limits
We blew up our engine
  Need to add an emergency defuel at redline engine speeds
We are destroying the engine
  Need to limit MGB speed for starting engine
We haven’t done that much control work
  Other ways to control the system?
Notes: Needs update